## Slide 1
Weather station
Cloud Gateway
IoT Device
Cloud
MXChip AZ3166 Devkit
IoT Hub
Stream Processing
Stream analytics
Cold path store
Data lake
Batch processing
Data lake analytics
Business integration
Azure function
Things
Insights
Actions
Cold path
Warm path

## Slide 2
System | Subsystem | Purpose
Weather station | IoT Device - MXChip AZ3166 Devkit | Connects directly (and securely) to the WIFI network in order to send the telemetry data in JSON format. Programmable in C/C++. Reacts to device twin updates and displays corresponding information.
Cloud | Cloud Gateway - IoT Hub | Ingests real-time data at a high rate and forwards it to the Stream analytics subsystem. Provisions the MXChip AZ3166 Devkit subsystem, along with its device twin.
Cloud | Stream processing - Stream analytics | Processes incoming data in real-time and directs it to the Data lake subsystem.
Cloud | Cold path store - Data lake | Close integration with the Data Lake analytics subsystem.
Cloud | Batch processing - Data lake analytics | Performs long-term data analysis by performing queries on historical data.
Cloud | Business integration - Azure function | Reacts to real-time input provided by the Stream analytics subsystem. Updates device twin properties. Programmable in C#/.NET